Department of Energy Science, Sungkyunkwan University

Suwon 16419, Republic of Korea

Tel: +82-31-299-4276 Fax: +82-31-299-6505

http://shb.skku.edu/catalysis

Sustainable Technologies for the Conversion of Biomass-Derived Materials to Value-Added Chemicals

Jung Woon Yang

Department of Energy Science, Sungkyunkwan University, Suwon 16419, South Korea

Email: jwyang@skku.edu

Homepage: https://shb.skku.edu/catalysis/

The depletion of the primary energy resources such as petroleum, coal, and natural gas has been a consistent concern, thereby leading to a sharper interest in bio-based products as promising alternatives to fossil-based products.[1] Bio-refinery technologies have emerged as an environmentally friendly way to obtain bio-based products from renewable and abundant biomasses, which is expected to bring significant environmental benefits and reduce dependence on petroleum.[2]

2,5-Furandicarboxylic acid (FDCA) is an important renewable building block used in diverse applications such as biofuels, solvents, drugs, and biopolymer monomers in bio-refinery technologies. Herein, unique strategy for the conversion of 5-hydroxymethylfurfural (HMF) to FDCA utilizing environmentally friendly vehicles such as NaOtBu-O2 system is described, and a pilot-scale (utilizing 1 kg HMF) study is conducted to evaluate the feasibility of the mass production of FDCA (Scheme 1).

In addition, a transition-metal-free chemoselective oxidative dehomologation of 2-O-benzylglycerol, which is derived from glycerol, into aromatic carboxylic acid and 2-(aryloxy)acetic acid is carried out by NaOtBu-O2 system. Furthermore, elaborative transformation of 2-(aryloxy)acetic acid to the unnatural -amino acid is investigated using potentially infinite natural resource such as (S)--amino acid in combination with sodium and molecular oxygen (Scheme 2).[3]

Details with the mechanistic investigation will be presented in this seminar.

References

- Tuck, C. O.; Pérez, E.; Horváth, I. T.; Sheldon, R. A.; Poliakoff, M. Science 2012, 337, 695.

- Maity, S. K. Renew. Sust. Energ. Rev. 2015, 43, 1427.

- Park, Y. J.; Yang, J. W. Green Chem. 2019, 21, 2615.